## Slide 1: Bay-Delta Water Quality Control Plan Update: San Joaquin River Flow and Salinity Objectives
State Water Resources Control Board

## Slide 2: Lower San Joaquin River (LSJR) Basin
San Joaquin River
Stanislaus River
Tuolumne River
Merced River
Stockton
Vernalis
Friant Dam
Modesto
Turlock
Merced
Notes: 4

## Slide 3: Four Key Points
Current Plan is out of date
Why focus on flow?
This is hard, requires balancing
Settlements are encouraged

## Slide 4
Proposed Flow Requirements
(Percent of Unimpaired Flow Feb-Jun)
= reservoir
= existing requirement
= proposed requirement
UF
UF
UF

## Slide 6
Iterate
Modeling Flow Chart
Water Supply Effects (WSE)
Core Model
  CEQA Impacts Analysis (20%/40%/60%)
  Surface Water Deficit
  Applied Water Needs
  Groundwater Use Estimates
  SWAP (StateWide Ag Production)
  IMPLAN Regional Economics
    (IMpact analysis for PLANning)
Outputs for Fish Benefits
Improved Temperature
Floodplain Habitat Inundation
HEC-5Q
Temperature
Model

## Slide 7: Programmatic Analysis
Quantitative information from models informs physical changes that could result from the plan amendments and have the potential for quantifiable impacts on environmental resources:
  River flows
  Reservoir operations
  Surface water diversions
  Groundwater pumping
Potential environmental impacts of these physical changes are evaluated in Chapters 5–17 of the SED

## Slide 8
If you would like to make a comment on the WQCP Update and SED you must send your comments by no later than 12:00 noon on
January 17, 2017 to: commentlettters@waterboards.ca.gov with “Comment Letter – 2016 Bay-Delta Plan Amendment & SED” in the subject line.
You can also make oral comments during the hearing held on:
For more information visit: http://waterboards.ca.gov/DeltaWQCP-Phase1
SACRAMENTO Nov. 29, 2016 and Jan. 3, 2017 – 9 AM CalEPA Headquarters Building 2nd Floor 1001 “I” Street | STOCKTON Dec. 16, 2016 – 9 AM Stockton Memorial Civic Auditorium Main Hall 525 “N” Center St,
MERCED Dec. 19, 2016 – 9 AM Multicultural Arts Center 645 W. Main Street | MODESTO Dec. 20, 2016 – 9 AM Modesto Centre Plaza Tuolumne River Room 1000 “K” Street

## Slide 10: Groundwater and Drinking Water
Technical State Water Board Staff/Community Water Interests meeting
November 18, 2016
State Water Board Panel:
Les Grober, Tim Nelson, Mark Roberson, Anne Huber, Yongxuan Gao, Will Anderson

## Slide 11: Topics Covered
Purpose
Overview Geographic Area
Agricultural Groundwater Assessment
  Method
  Assumptions and Data Sources
  Results
Analysis of Potential Impact to Drinking Water
  Context
  Potential impacts
  Sources of Funding

## Slide 12: Purpose of the Groundwater Analysis
Purpose
  To estimate the relative effects of the LSJR alternatives on the groundwater subbasins.
  To support other quantitative and qualitative analyses throughout the Substitute Environmental Document (SED).

## Slide 13: Groundwater-Related Assessments
Groundwater modeling (Appendix G)
Existing groundwater conditions and groundwater as a resource (storage, quality, subsidence – Ch 9)
Agriculture (Ch 11)
Service providers (groundwater quantity and quality – Ch 13)
Greenhouse gases (energy consumptions and GHG emissions from increased Groundwater pumping – Ch 14)
Economics (Ch 20)
Possible management options for municipal and domestic water supply (Ch 22)

## Slide 14: Analytical Framework of the Modeling
Surface water diversions could be reduced in implementing the proposed unimpaired flow requirements
If possible affected water users would increase groundwater pumping to compensate for lost surface water
Groundwater tables could fall, which could affect wells used to supply drinking water
Groundwater pumping would currently be limited by infrastructure capacity, in the future it may be limited by the Sustainable Groundwater Management Act (SGMA)

## Slide 15
Groundwater Subbasin
  Merced
  Turlock
  Modesto
  Eastern San Joaquin
Irrigation Districts:
  Merced (MeID)
  Turlock (TID)
  Modesto (MoID)
  Oakdale (OID)
  South San Joaquin (SSJID)
  Central San Joaquin Water Conservation District (CSJWCD)
  Stockton East Water District (SEWD)

## Slide 16: In District Groundwater Balance
Distribution System
Irrigated Crops
Groundwater Subbasin
Municipal Use
Tributary
Crop Consumptive Use of Applied Water
Applied Groundwater
(District + Private Pumping)
Deep Percolation
System Seepage
Surface Water Diversion
Evaporation
Applied Surface Water
Surface Water Returns
Irrigation District

## Slide 17: Groundwater Subbasin Balance
Distribution System
Irrigated Crops
Groundwater Subbasin
Applied Groundwater
Deep Percolation
System Seepage
Irrigation Districts
Residential and Industrial Use
Municipal Use
Irrigated Crops
Applied Groundwater
(Private Pumping)
Crop Consumptive Use of Applied Water
Crop Consumptive Use of Applied Water
Non-ID Agriculture
Municipal Wells
Deep Percolation
Wastewater
Surface Water Diversion

## Slide 18: Agricultural Groundwater Use Analysis Key Assumptions
Within the Irrigation Districts:
  Groundwater pumping occurs at the farm gate and is only used to satisfy crop applied water demand
  Assume districts can pump as much groundwater as needed, up to their maximum pumping capacity
  For SEWD and CSJWCD only the portion of water that they contract for on the Stanislaus (totals 155 TAF) is modeled, assuming both districts can fully replace any shortage with groundwater.
Areas outside of the Districts, but within the groundwater subbasins:
  Includes estimates of municipal pumping based on the 2003 Bulletin 118
  Assume agricultural areas are supplied by groundwater, with a few exceptions

## Slide 19: Agricultural Groundwater Use Analysis Data Sources
Parameters based on district AWMPs and September 2015 information request responses
  District M&I deliveries
  Seepage from regulating reservoirs
  Minimum annual groundwater pumping
  Maximum Groundwater Pumping Capacity
  Distributions loss factors
  Deep percolation factors

## Slide 20: Agricultural Groundwater Use Analysis Surface Water Replacement
Chart: Applied Groundwater and Surface Water for Merced ID under Baseline Conditions
See page G-24 Appendix G figure G.2-2A

## Slide 21: Agricultural Groundwater Use Analysis Surface Water Replacement
Chart: Applied Groundwater and Surface Water for Merced ID with a 40% unimpaired flow Objective on the Merced River
See page G-26 Appendix G figure G.2-2C

## Slide 22: Average Annual Groundwater Pumping
Chart: Modeled Groundwater Pumping across all Irrigation Districts
| All Year Types | Wet | Above Normal | Below Normal | Dry | Critically Dry
Baseline Conditions | 260 | 185 | 203 | 228 | 221 | 485
40% Unimpaired Flow Objective | 364 | 192 | 235 | 376 | 524 | 614
Estimated 2009 Maximum Groundwater Pumping Capacity = 626 TAF/y

## Slide 23: Average Annual Groundwater Recharge
Chart: Modeled Groundwter Recharge across all Irrigation Districts
| All Year Types | Wet | Above Normal | Below Normal | Dry | Critically Dry
Baseline Conditions | 728 | 713 | 745 | 774 | 793 | 646
40% Unimpaired Flow Objective | 648 | 711 | 723 | 694 | 631 | 457

## Slide 24: GW Net Input within the Districts
Chart: Annual Average Net Input to GW for each Irrigation District
| Baseline | 20% UF | 30% UF | 40% UF | 50% UF | 60% UF
SSJID | 33.7437 | 28.7649 | 25.8434 | 18.3953 | 10.8066 | 1.1937
OID | 64.917 | 59.7159 | 56.5286 | 48.7895 | 39.8828 | 29.0805
MoID | 49.4255 | 47.338 | 42.5496 | 35.1242 | 27.4124 | 15.897
TID | 106.6216 | 100.827 | 87.8563 | 67.4354 | 46.1765 | 14.5476
MeID | 100.4076 | 70.8064 | 47.403 | 19.2106 | -14.1629 | -51.1173

## Slide 25: Potential Impacts to Drinking Water

## Slide 26: Drinking Water Supply in the Four Subbasins
Population: 1.25 million (U.S. Census Bureau 2010)
1.12 million are connected to public water systems
133,000 rely on domestic (private) wells
Chart: Population Served by Public and Private Sources in the 4 Subbasins
| Public Water System | Private Well
 | 1120000 | 133000

## Slide 27: Drinking Water Supply in the Four Subbasins (cont.)
93 public water suppliers delivered 323 TAF water in 2014
  Groundwater: 169 TAF
  Surface water: 154 TAF
Domestic wells: 38 TAF
Total water production in : 323 + 38 = 361 TAF
Chart: Population Served by Public and Private Sources in the 4 Subbasins
Chart: Public Water Supply and Sources in 2014 in the 4 Subbasins
| Public: GW | Public: SW
 | 168.5641 | 154.0471
Chart: Overall Water Supply and Sources in 2014 in the 4 Subbasins
| Public: GW | Public: SW | Private: GW
 | 168.5641 | 154.0471 | 38

## Slide 28: Potential Impacts on Drinking Water
May need to deepen existing wells or build more wells
May increase pumping cost
Could degrade groundwater quality
Could make groundwater unavailable in some areas

## Slide 29: Potential Effect on Groundwater Overdraft
LSJR Alt 3 (40% UF): 186 TAF/y
Current rate of overdraft: 155 TAF/y
Total groundwater storage: 125 MAF (estimate made in 1960s; Williamson et al. 1989)
Actions are needed to address groundwater overdraft with or without the proposal

## Slide 30: Current Estimated Rates of Groundwater Overdraft
Subbasin | From Ch 9 (TAF/y) 1 | From ExeSum (TAF/y) 2
Eastern San Joaquin | 88 | 50
Turlock | 9 | 21.5
Modesto | 11 | Assumed to have same combined rate as the above two
Merced | 44 | 
Total | 155 | 144
1 Calculated using average annual groundwater level decline between 1970 and 2000 × subbasin area × estimated average specific yield as reported California’s Groundwater Bulletin 118, Update 2003 2 Calculated assuming Modesto and Merced has the same combined rate of overdraft as Eastern San Joaquin (ESJ) and Turlock. Number for ESJ was reported in California’s Groundwater Bulletin 118, Update 2003 and that for Turlock was reported in TGBA 2008 |  | 

## Slide 31: Potential Groundwater Quality Impacts
Reduction in groundwater level could:
  Accelerate migration of surface contaminants to the well
  Cause saline water intrusion to the aquifer
  Mobilize naturally-occurring trace elements and elevate their concentrations in the aquifer
It is speculative to determine the impact from increased groundwater pumping
  Depends on many variables
  Not possible to predict how the affected parties would respond

## Slide 32: Public Water Suppliers
A substantial increase in groundwater pumping would not necessarily result in violation of drinking water quality standards because recent data do not indicate increased water quality standard violations in public water systems despite greatly increased groundwater pumping
Service providers are required to take actions to ensure that the water is in compliance with relevant drinking water standards before it is served to the public

## Slide 33: Domestic Wells
Increased pumping could affect groundwater flow and quality, depending on many unknown factors
  This could affect domestic wells
No systematic monitoring of domestic wells
  Testing well water and other best practices set forth in SED are important
Important for local groundwater sustainability agencies to implement SGMA both for overpumping and water quality degradation

## Slide 34: Example Financial Assistance from the State Water Board
Public Water System Drought Emergency Response
  e.g. 2015, Plainsburg Elementary School in Merced County, $180,882
Drinking Water State Revolving Fund (DWSRF)
  e.g. 2015, City of Hughson in Stanislaus County, $6,607,210
Proposition 1- administered as a part of DWSRF

## Slide 35: Further Information
More information on these topics can be found in the following chapters and appendices of the SED:
  Chapter 9, Groundwater Resources
  Chapter 13, Service Providers
  Chapter 22, Integrated Discussion of Potential Municipal and Domestic Water Supply Management Options
  Appendix G, Agricultural Economic Effects of the Lower San Joaquin River Flow Alternatives: Methodology and Modeling Results
These chapters, as well as the Groundwater and Surface Water Use Analysis spreadsheet, can be found at:
http://www.waterboards.ca.gov/waterrights/water_issues/programs/bay_delta/bay_delta_plan/water_quality_control_planning/2016_sed/index.shtml.

## Slide 37: Economic Impacts
Technical State Water Board Staff/Community Water Interests meeting
November 18, 2016
State Water Board Panel:
Les Grober, Tim Nelson, Tom Wegge, Dan Worth, Mark Roberson, Nicole Williams

## Slide 38: Economic Analyses: Topics Covered
Regulatory Requirements
Analytical Framework & Resources Evaluated
Study Area(s)
Types of Evaluations
Agricultural Economic Evaluation
  SWAP: Sources of Data, Model Description, Assumptions, and Study Area
  IMPLAN Multipliers: Sources of Data, Assumptions, and Study Area

## Slide 39: Economic Analyses: Regulatory Analytical Requirements
CEQA
  Requires economic effects linked to a physical change
  Allows lead agency to include more information
Porter Cologne Act (CA Water Code)
  Section 13141: estimate of “total cost of a program” and “potential sources of financing”
  Section 13241: consider “economic considerations” – in practice, costs to affected parties and potential impacts on local and regional economies

## Slide 40: Economic Analyses: Analytical Framework
Purpose
To compare potential economic effects of predicted changes in surface water diversions across the LSJR alternatives
Analysis Goal
To help inform the State Water Board’s consideration of potential changes to the 2006 Bay‑Delta Plan related to LSJR flow objectives

## Slide 41: Economic Analyses: Resources Evaluated
Lower San Joaquin River and Tributaries
Changes in Hydrologic Conditions
Agricultural Production and Related Effects on the Regional Economy and Local Fiscal Conditions
Municipal and Industrial Water Supplies and Affected Regional Economies
Hydropower Generation, Revenues and the Regional Economy
Fisheries and Associated Regional Economies
Recreational Opportunities, Activity, and the Regional Economy
In addition, costs of non-flow measures are considered

## Slide 42: Economic Analyses: Study Area(s)
Vary by resource topic
temporal and geographic characteristics of affected resources
geographic extent of effects on local and regional economies
Includes Areas beyond the Plan Area
e.g., commercial and recreational fisheries, water supply

## Slide 43: Economic Analyses: Types of Evaluations
Direct and indirect effects at the local and/or regional level
Qualitative and quantitative assessments
For quantitative analyses, different analytical tools used
EXAMPLE: Agricultural Production and Related Economic Effects |  | 
Resource | Type of Evaluation | Analytical Tool
Hydrologic & Water Supply | Quantitative | Water Supply Effects Model
Agricultural production | Quantitative | SWAP
Regional agricultural effects | Quantitative | IMPLAN multipliers
Fiscal effects related to agriculture | Quantitative and Qualitative | IMPLAN multipliers and data from three county region

## Slide 44: Agricultural Economic Analysis
Given the proposed unimpaired flow objectives there will likely be more frequent agricultural water shortages
As a result, crop production could be lower in certain years, particularly during drier periods.
Fallowing of crops will reduce their gross revenues. Some changes in prices and adjusting of cropping patterns may dampen this effect.
Reduced revenue could cause some jobs related to the crop production to disappear.
Other economic sectors may also see revenue and employment impacts related to impacts in the agricultural industry.

## Slide 45
Agricultural Groundwater Use Analysis
SWAP (Agricultural Production)
IMPLAN Multipliers
(Region -Wide Effects)
Water Supply Effect (WSE)
Changes in
Employment
Total Sector Output
Value-Added
Changes in
Agricultural Revenues
Cropping Patterns
INPUTS
MODEL
OUTPUT
Suite of Models for Studying Economic Impacts in Agriculture
Changes in
Surface Water Availability
Changes in
Groundwater Pumping
Potential UF Requirements
Change in Applied Surface Water
Change in Crop Applied Water
Change in Agricultural Revenues

## Slide 46: Agricultural-Economic Analysis SWAP Model
  Agricultural –Economic optimization model that assumes farmers operate to maximize net economic returns
  Developed in the 1990s and constantly updated
  Covers most agriculture in the state
Inputs: base cropping patterns, water use intensity, total land and water use
  Outputs: agricultural production acreage, crop revenue, optimized cropping patterns
Has been used to study agricultural response to:
  Water scarcity
  Salinity

## Slide 47: Agricultural-Economic Analysis Model Setup
Agricultural Impact Analysis (using SWAP):
  Analysis covers six areas representing each of the 7 irrigation districts that receive surface water from the east side tributaries (with SEWD and CSJWCD combined)
  19 crop categories following DWR classification for land and water use
  Base land and applied water are calibrated to 2010 levels using DWR DAU Crop Surveys for 2010

## Slide 48: Total Applied Water
Applied Water (AW) refers to water used to irrigate crops from either groundwater pumping, surface water diversions, or both.
 | Average Annual Applied Water Demand (TAF/y) |  |  |  |  | 
 | All Year types | Wet | Above Normal | Below Normal | Dry | Critically Dry
Crop Applied Water Demand | 1604 | 1483 | 1565 | 1643 | 1696 | 1720
 | Average Annual Applied Water Deficit (TAF/y) |  |  |  |  | 
Baseline Conditions | 45 | 0 | 0 | 0 | 9 | 224
30% UF Objective | 111 | 0 | 0 | 23 | 90 | 477
40% UF Objective | 182 | 4 | 37 | 104 | 230 | 618
50% UF Objective | 276 | 13 | 83 | 241 | 412 | 780
TAF = Thousand Acre Feet per year UF = Unimpaired Flow Average Annual applied water demand and deficits for the 7 irrigation districts combined |  |  |  |  |  | 

## Slide 49: Total change in Acreage
Chart: Annual Average Irrigated Acres over all Irrigation Districts
| Baseline | 20% UF | 30% UF | 40% UF | 50% UF | 60% UF
All Years | 512229.2238 | 506143.6984 | 500401.4583 | 488808.3285 | 468809.4715 | 441589.2707
Critically Dry Years | 488544.2671 | 458641.1556 | 438611.2836 | 409440.3703 | 368327.5312 | 340247.5859

## Slide 50: Agricultural-Economic Analysis Crop Revenue Impacts within Districts
Chart: Annual Average Revenue from Crop Production over all Irrigation Districts
| Baseline | 20% UF | 30% UF | 40% UF | 50% UF | 60% UF
All Years | 1477075111.7418 | 1467591264.9104 | 1458530159.4537 | 1440833976.6163 | 1406733719.7024 | 1360184846.5032
Critically Dry Years | 1437842203.6041 | 1391442460.5689 | 1360980827.5519 | 1317886448.0126 | 1238425040.8133 | 1180938104.0993

## Slide 51: Regional Economic Analysis
IMPLAN is an Input-Output model that provides a snapshot of a region’s economy
Regional Economic Analysis
  Uses marginal multipliers derived from IMPLAN model that relate the direct change in crop revenue output from SWAP to the change in revenue and employment for other industries.
  IMPLAN data from 2010
  Analysis covers the three county area of Merced, Stanislaus, and San Joaquin Counties
  8 IMPLAN crop categories

## Slide 52: IMPLAN Multipliers
Changes in SWAP revenue output represent direct revenue impacts associated with reduced crop production
IMPLAN contains multipliers to estimate indirect and induced impacts
  Indirect impacts could result in industries that provide inputs to the agricultural industry
  induced impacts could result because of the changes in spending throughout the economy as labor income has changed

## Slide 53: Regional Economic Impacts
Economic Effects | Baseline Total Economic Output | Change from Baseline ($ Millions, 2008) |  | 
 | ($ Millions, 2008) | 30% Unimpaired Flow Objective | 40% Unimpaired Flow Objective | 50% Unimpaired Flow Objective
Direct Effects | $1,477 | -$19 | -$36 | -$70
Indirect and Induced Effects | $1,109 | -$14 | -$27 | -$53
Total Sector Output | $2,586 | -$33 | -$64 | -$124
% of Baseline Total Economic Output | 100% | -1.3% | -2.5% | -4.8%
Table G.5‑4. Average Annual Total Economic Output Related to Agricultural Production in the Irrigation Districts under Baseline Conditions and the Change for Each of the LSJR Alternatives (page G-67)
Modified from Table G.5-4, Page G-67 of Appendix G

## Slide 54: Regional Employment Impacts
Employment Effects | Baseline Total Economic Output | Change from Baseline (# of Jobs) |  | 
 | (# of Jobs) | 30% Unimpaired Flow Objective | 40% Unimpaired Flow Objective | 50% Unimpaired Flow Objective
Direct Employment | 8,097 | -99 | -190 | -406
Indirect and Induced Employment | 10,514 | -124 | -242 | -471
Total Employment | 18,601 | -224 | -433 | -877
% of Baseline Total Employment | 100% | -1.2% | -2.3% | -4.7%
Table G.5‑6. Average Annual Total Employment Related to Agricultural Production in the Irrigation Districts under Baseline Conditions and the Change for Each of the LSJR Alternatives (page G-70)
Modified from Table G.5-6, Page G-70 of Appendix G

## Slide 55: Further Information
More information on these topics can be found in the following chapters and appendices of the SED:
  Chapter 11, Agricultural Resources
  Chapter 20, Economic Analysis
  Appendix G, Agricultural Economic Effects of the Lower San Joaquin River Flow Alternatives: Methodology and Modeling Results
These chapters, as well as the Agricultural Economic Analysis spreadsheet, can be found at:
http://www.waterboards.ca.gov/waterrights/water_issues/programs/bay_delta/bay_delta_plan/water_quality_control_planning/2016_sed/index.shtml.

## Slide 56: Extra slides…

## Slide 57: Current Plan Out of Date
Plan last updated 21 years ago in 1995
Species have been declining – the need for update was identified 10 years ago (in 2006 Plan update)
Endangered Species Act increasing water restrictions
Administration’s California Water Action Plan directs the State Water Board to complete the update of the Plan to further achievement of the co-equal goals in the Delta

## Slide 58: Why Focus on Flow?
Scientific studies show that flow is a major factor in the survival of fish like salmon
Many benefits of flow, including improved growth and survival of native fish by improving water temperatures and increasing floodplain habitat
Flow affects risk of disease, risk of predation, reproductive success, growth, smoltification, migration, feeding behavior, and other ecological factors
Non-flow measures can also be important but State Water Board has limited authority to require non-flow measures

## Slide 59: This is Hard, Requires Balancing
State Water Board’s 2010 flow criteria report – a purely technical assessment and no balancing – concluded that 60 percent of flow should be left in the LSJR for the benefit of fish
Current uses (agriculture, drinking water) rely on up to 80 percent or more of the unimpaired flow
Unlike the 2010 report, this staff proposal considers other uses and aims to strike a balance among competing uses of water
The staff proposal recommends a range of between 30 and 50 percent of unimpaired flow, with a starting point of 40 percent – this is a big increase

## Slide 60: This is Hard, Requires Balancing
This is less than what environmental and commercial fishing interests favor, and more than agricultural and affected urban users want
Balancing is hard, but is what we are called upon to do
Because it is hard, State Water Board has a long history of encouraging settlements.

## Slide 61: Settlements are Encouraged
The flow proposal includes “adaptive implementation,” which allows adjustments so water is used wisely and more effectively – implementation of non-flow measures could also reduce the flows needed
Board is looking for durable local solutions that will improve flows and other conditions that can reduce the need for flow
Local water agencies and local people working with agency experts and other organizations can provide the foundation for such durable solutions
The California Natural Resources Agency is leading settlement discussions to explore the potential for a comprehensive agreement on environmental flows in both the San Joaquin and Sacramento River basins

## Slide 62: Current SJR Spring Flow Objective
One compliance location: Lower San Joaquin River at Vernalis (inflow to Delta)
Minimum monthly average flow rates
Includes "pulse" flow during a 31-day period in April and May of each year
USBR only responsible water right holder

## Slide 63: Proposed LSJR Flow Objective
Applies to the Stanislaus, Tuolumne, and Merced Rivers
Narrative Objective:
  Maintain inflow conditions from the SJR watershed to the Delta at Vernalis sufficient to support and maintain the natural production of viable native SJR fish populations migrating through the Delta
Numeric Objective:
  Feb - June: 30% - 50% unimpaired flow
  Starting point of 40%
  Unimpaired flow: the natural water production of a river basin, unaltered by upstream diversions, storage, or by export or import of water to or from other watersheds

## Slide 64: Proposed LSJR Flow Objective
Adaptive Implementation
  Adjustments within the 30% - 50% range
  Adjustments within Feb - June period
  Flow shifting to avoid temperature impacts in fall
Stanislaus, Tuolumne, and Merced (STM) Working Group – implementing entity
  Biological goals
  Planning, monitoring, and reporting
  Voluntary agreements

## Slide 65: Current Southern Delta Salinity Objective
April through August: 0.7 millimhos per centimeter (mmhos/cm) EC
  based on the salt sensitivity and growing season of beans
September through March: 1.0 mmhos/cm EC
  based on the growing season and salt sensitivity of alfalfa during the seedling stage
4 Salinity compliance stations within the south Delta:
  San Joaquin River at Vernalis
  San Joaquin River at Brandt Bridge
  Old River at Middle River
  Old River at Tracy Road Bridge.
Hoffman Report, Figure 1.1.

## Slide 66: Proposed Southern Delta Salinity Objective
Year round objective of 1.0 deciSemens per meter (dS/m) EC
Three compliance locations changed to channel segments
  SJR from Vernalis to Brandt Bridge
  Middle River from Old River to Victoria Canal
  Old River/Grant Line Canal from Head of Old River to West Canal
Continued conditions in USBR and DWR’s water rights
  USBR - 0.7 EC at Vernalis April - Aug; 1.0 EC Sep - March
  DWR & USBR - 1.0 EC year round in the interior Delta locations
  DWR & USBR - Continued operations of agricultural barriers or other reasonable measures to address impacts of SWP/CVP operations on water levels and flow conditions
Other Requirements
  Comprehensive Operations Plan - Information, actions, performance goals to address SWP/CVP export operations on water levels and flow conditions affecting salinity
  Monitoring and reporting
  Study to characterize dynamics of water level, flow, and salinity conditions
LSJR flow objectives would improve salinity conditions

## Slide 67: Instream Flows Under the Flow Proposal
Under the 40% unimpaired flow (UF) proposal, average annual instream flow Feb - June would increase by 288 thousand acre feet (TAF), or 26 percent.

## Slide 68: Ecosystem Benefits of the Flow Proposal
Restores the pattern and some limited magnitude of flow that are more closely aligned to the flow conditions to which native species are adapted
Improves attainment of temperature criteria and increases floodplain inundation, resulting in greater survival and resiliency of native fish

## Slide 69: What are the Impacts of the Flow Proposal?
The greatest impact on diversions for human use would be in driest years; there would be almost no impact on diversions for human use in wet years.

## Slide 70: What are the Impacts of the Flow Proposal?

## Slide 71: What are the Impacts of the Flow Proposal?

## Slide 72: What are the Impacts of the Flow Proposal?

## Slide 73: What are the Impacts of the Flow Proposal?
Implementing the 40% flow proposal could result in:
14% reduction (293 TAF) in water available for surface water diversion (7% to 23% reduction for 30% to 50% range of unimpaired flow)
Increase groundwater pumping by an average of 105 thousand acre-feet per year (TAF/yr)
Increase unmet agricultural water demand by 69 TAF/yr (2014 baseline GW pumping) to 137 TAF/yr (2009 baseline GW pumping) in the plan area
An average annual decrease in economic output of $64 million (2.5% reduction from baseline annual average agricultural economic sector output of $2.6 billion)

## Slide 74: Phase 1 Next Steps
Public Hearing Dates:
  Nov 29: Sacramento
  Dec 16: Stockton
  Dec 19: Merced
  Dec 20: Modesto
  Jan 3: Sacramento
Technical Workshops: December 5th and 12th, Sacramento
Draft SED & Plan Comments due: Jan 17, 2017
Release Final SED & Plan: May 2017
Board meeting to adopt: July 2017

## Slide 75
If you would like to make a comment on the WQCP Update and SED you must send your comments by no later than 12:00 noon on
January 17, 2017 to: commentlettters@waterboards.ca.gov with “Comment Letter – 2016 Bay-Delta Plan Amendment & SED” in the subject line.
You can also make oral comments during the hearing held on:
For more information visit: http://waterboards.ca.gov/DeltaWQCP-Phase1
SACRAMENTO Nov. 29, 2016 and Jan. 3, 2017 – 9 AM CalEPA Headquarters Building 2nd Floor 1001 “I” Street | STOCKTON Dec. 16, 2016 – 9 AM Stockton Memorial Civic Auditorium Main Hall 525 “N” Center St,
MERCED Dec. 19, 2016 – 9 AM Multicultural Arts Center 645 W. Main Street | MODESTO Dec. 20, 2016 – 9 AM Modesto Centre Plaza Tuolumne River Room 1000 “K” Street